| For Release: | April 19, 2005 |
| --- | --- |
| Contact: | David J. Buchko Product Communications Manager 201-307-3789 / dave.buchko@bmwna.com William Scully BMW Product Communications Specialist 201-307-3790 / william.scully@bmwna.com |

THE ALL-NEW BMW 3 SERIES SPORTS WAGON

Dynamic, Elegant, Practical

Woodcliff Lake, NJ – April 19, 2005… The all-new BMW 3 Series Sports Wagon will make its public debut at the Frankfurt Motor Show in September 2005.  With an exceptional harmony of elegance and athleticism, the Sports Wagon offers flexibility and practicality as well.  Available in the US beginning in October 2005, the newest BMW Sports Wagon will continue the  highly successful tradition of combining more versatile cargo space with the performance and handling of a sports sedan.

This latest generation sports wagon will initially be available in the U.S. as a 325xi model.   Its xDrive all-wheel drive system endows it with remarkable traction and agility.  The all-new 3 Series Sports Wagon family will expand in 2006 with the introduction of a rear wheel drive version.

Efficient and sporting

Like the all-new 325i Sedan, the Sports Wagon will be powered by BMW’s new, advanced N52 3.0 liter 6-cylinder engine.   This dynamic powerplant  retains the unique smoothness and sound character of BMW’s inline 6-cylinder format while offering more power, greater torque, even more refined delivery of power, and new technology.  This includes magnesium/aluminum composite engine construction, and BMW’s patented Valvetronic variable valve lift system, which replaces the conventional throttle for more efficient  engine breathing and improved responsiveness.  The 325i Sports Wagon is equipped with a new, standard six-speed manual gearbox ; an optional six-speed STEPTRONIC automatic transmission is available.

Unique and sophisticated design

For the first time, the BMW 3 Series Sports Wagon has been developed as an entirely different and unique car compared to the Sedan.  The new Sports Wagon is largely identical to the Sedan from the front all the way to the A-pillar; the rear seat area and luggage compartment blend harmoniously with the overall style of the car’s sporting, almost coupe-like silhouette.  One distinctive design element is the side window area. The roofline tapers down softly and smoothly to the inclined tailgate, while the shoulder line moves up slightly, the window areas appear small and compact, as in a coupe.

More room than its predecessor

While the new 325xi Sports Wagon maintains the BMW heritage in both styling and performance – powerful, sporting, compact – it is equally impressive in its space and roominess.  Length (+1.65“), width (+3.07“), height (+0.35“), and wheelbase (+1.38“) are all increased compared to the previous generation Sports Wagon, providing front and rear occupants with additional space and comfort on the road.  The split-folding rear seats and large cargo area offer a high degree of flexibility and utility.

Innovative equipment for even greater practical value

The 325xi Sports Wagon is provided with a number of innovative features that not only enhance  everyday driving qualities, but the practical benefits of this unique model as well.  For example, the luggage compartment cover ensures privacy and automatically rises together with the separately opening rear window in order to facilitate loading.  Like the all-new 3 Series Sedans, the Sports Wagon comes with run-flat tires and a Flat Tire Monitor. The lack of a spare tire not only reduces the weight of the car but increases effective cargo capacity, with an additional storage box beneath the floor of the luggage compartment.

The luggage compartment floor section is  available with two reversing surfaces, with tie-down points on one side to securely fasten heavy objects, and a plastic cover on the other side to be placed on the interior panels and surfaces in the luggage compartment to ensure efficient protection from dirt and scratches.  A water-tight folding box beneath the floor of the luggage compartment enables the storing of items such as wet boots or other gear.

BMW’s traditional attention to detail is evident with available sunshades on the rear side windows which are unusal in this vehicle category, as are the separate rear seat air vents.

Safety engineering and features: improving on a star performer

New Head Protection System (HPS).  The first front-to-rear Head Protection System to be offered in the 3 Series employs a curtain-type system, which takes up less space in the headliner and can remain inflated for several seconds after deployment, especially important in case of rollover.

New seat-mounted front side-impact airbags.  The 3 Series is BMW’s first to employ seat-mounted side-impact airbags, as opposed to the door-mounted type of the predecessor and other current Series.  In their function of protecting occupants’ pelvis and thorax regions in side impacts, the seat-mounted airbags are equal to the door-mounted type, but offer greater freedom for the interior designers to achieve their functional and esthetic goals.

Automatic safety-belt tensioners and force limiters front and rear. Long standard on BMW front safety belts, these features now enhance the outboard rear belts’ effectiveness as well.

New occupant-detection sensor. BMW has long employed a sophisticated electronic control strategy for managing the deployment of airbags and safety-belt tensioners.  This approach to optimal effectiveness of safety systems now becomes even more precise, thanks to a new sensing mat in the front passenger seat.  Called OC3, the mat is more highly sophisticated than its predecessor; it measures the weight and analyzes the pressure distribution of the occupant in order to distinguish between an adult and an infant in a child safety seat.  The front passenger’s airbags will be deactivated, should the driver install a forward-facing infant safety seat.

New features for protecting the driver’s feet and knees. Two measures have been taken to reduce the likelihood of injuries to the driver’s feet and legs:

•	The footrest is designed to crush under the force of the driver’s left foot in certain frontal impacts, so that the full impact force is not transmitted to his or her foot and leg.

•	The Mastervac (brake master cylinder) is mounted so that as the front end deforms, it rotates, and with it the brake and clutch pedals. The pedals move forward, canceling much of the force transfer to the driver’s feet and legs if they are on the pedals.

And for the first time, the 3 Series Sports Wagon offers LATCH attachments on the front passenger’s seat as well as the two outboard rear seats for optimum safety with up to three children in the car.

Complete with Panorama Roof for a unique open-air experience

A wide range of creature comforts enhances the versatility of the 3 Series Sports Wagon: the panorama roof, for example, virtually changes this practical touring car into a convertible.  Almost two feet  longer than a conventional sliding roof, the panorama roof lets in up to 60 per cent more fresh air.

Handling and agility – raising the standard again

The BMW 3 Series Sports Wagon is first and foremost a BMW 3 Series, combining a comfortable ride with sports car handling.  It is a very dynamic car on the road, with that recognizable “BMW feel”.  Near 50-50 weight distribution, all-wheel drive, a long wheelbase, and short body overhangs front and rear are simply ideal for outstanding agility and driving safety under any circumstances.

The double-pivot front suspension, newly developed for the 3 Series Sedan, offers an optimum balance of driving dynamics and ride comfort in the Sports Wagon as well. Utilizing extensive aluminum componentry, this innovative suspension design offers superior tracking stability and low unsprung weight.  Class-leading agility and dynamic handling, in turn, are ensured by the five-link rear axle in lightweight steel, ensuring precise wheel guidance as well as excellent roll comfort.

Active Steering: Unique in this Class

The optional Active Steering system, a BMW first, offers two significant benefits:

•	Widely variable steering ratio; steering-wheel movements for parking maneuvers, U-turns and sharp corners are greatly reduced for amazing agility.  With increasing vehicle speed, the steering becomes “slower,” favoring stability over agility.

•	Vehicle stabilization; in critical situations, Active Steering can intervene to preserve stability.  For example, if the driver applies the brakes while driving on a surface with uneven traction (one side of the road slick, the other grippy), Active Steering can recognize the effects of varying traction and steer to compensate.

Latest-Generation DSC

BMW’s Dynamic Stability Control (DSC), featured here in its latest generation, helps  ensure extraordinary safety on the road.  New for 2006 is a wide array of important functions that make driving even safer and more pleasant. They are:

•	Brake Fade Compensation. Brake fade occurs as the brakes heat up under hard use; a given degree of deceleration requires more pressure on the brake pedal. As brake temperature rises, Brake Fade Compensation automatically compensates by increasing the hydraulic pressure relative to pedal force.

•	Brake Stand-by. When the driver lifts off the accelerator pedal abruptly, DSC recognizes that sharp braking may be about to occur and applies just enough pressure in the brake system to snug up the pads against the rotors.  Thus, the short lag time which normally results from bringing the pad to the rotor is dramatically decreased. The reduced stopping or deceleration distance could reduce the likelihood of an accident.

•	Brake Drying. Acting on input from the rain sensor (an element of the standard rain-sensing windshield wipers), the pads are periodically brought up to the rotors – just enough to eliminate any film of water between pads and rotors, but not enough to cause a brake application.

•	Comfort Stop. Especially with an automatic transmission, unless the driver consciously eases off on the brake pedal, a jerk can occur as the vehicle comes to a stop.  Comfort Stop automatically eases off, making for smoother stops.

•	Start-off Assistant. Keeps the vehicle from rolling backward when stopped facing uphill. The driver can then start up without doing a ballet with the clutch, brake and accelerator (manual transmission) or doesn’t have to hold the accelerator or brakes while stopped on a hill (automatic transmission).

## With all these features, the MSRP of the 325xi Sports Wagon is $34,695.  A typically equipped Sports Wagon includes the Premium Package, an automatic transmission, leather upholstery and metallic paint.  At $39,345, a typically equipped 2006 325xi Sports Wagon is only $200 more than its 2005 counterpart and has substantially more equipment.

## BMW Group In America

BMW of North America, LLC has been present in the United States since 1975.  ROLLS-ROYCE Motor Cars NA, LLC began distributing vehicles in 2003.  The BMW Group in the United States has grown to include marketing, sales, and financial service organizations for the BMW brand, the MINI brand, and the ROLLS-ROYCE brand of Motor Cars; DesignworksUSA, an industrial design firm in California; a technology office in Silicon Valley and various other operations throughout the country.  BMW Manufacturing Co., LLC in South Carolina is part of BMW Group’s global manufacturing network and is the exclusive manufacturing plant for all Z4 Roadster and X5 Sports Activity Vehicles. The BMW Group sales organization is represented in the U.S. through networks of 340 BMW passenger car centers, 327 BMW Sports Activity Vehicle centers, 148 BMW motorcycle retailers, 80 MINI passenger car dealers, and 25 ROLLS-ROYCE Motor Car dealers.  BMW (US) Holding Corp., the BMW Group’s sales headquarters for North, Central and South America, is located in Woodcliff Lake, New Jersey.

Information about BMW Group products is available to consumers via the Internet at:

www.bmwusa.com

www.bmwmotorradusa.com

www.miniusa.com

www.rolls-roycemotorcars.com

Journalist note: Information about the BMW Group and its products is available to journalists on-line at the BMW Group PressClub at the following address: www.press.bmwgroup.com.

#      #      #