| For Release: | May 22, 2006 |
| --- | --- |
| Contact: | David J. Buchko Product Communications Manager 201-307-3789 / dave.buchko@bmwna.com William Scully BMW Product Communications Specialist 201-307-3790 / william.scully@bmwna.com |

### 2006 BMW M ROADSTER

# Technical Specifications

## General

Curb weight, lb.	3197

Weight distribution, front/rear, %	50.7/49.3

Wheelbase, in.	98.3

Track, front/rear, in.	58.5/59.7

Length, in.	161.9

Width, in.	70.1

Height, in. (with softtop up)	51.3

## Body

Type	2-seat Roadster

Aerodynamic drag coefficient	0.38 (with softtop up)

EPA size classification	2-Seater

## Accommodations

Seating capacity, persons	2

Shoulder room, in.	52.5

Head room, in.	37.3 (with softtop up)

Leg room, in.	42.0

EPA interior volume, cu ft.	47.6 (with softtop up)

Cargo volume, cu ft.	7.1/7.8

## Engine & electrical

Engine type	DOHC inline 24-valve 6-cylinder,

high-pressure Double VANOS

steplessly  variable intake- &

exhaust-valve timing, 6 individual

electronically controlled throttles with

Normal & Sport settings

Bore x stroke, mm/in.	87.0 x 91.0/3.43 x 3.58

Displacement, cc/cu in.	3246/198

Compression ratio	11.5:1

Power @ rpm, hp	330 @ 7900

Torque @ rpm, lb-ft.	262 @ 4900

Engine-management system	MSS70 with knock control); variable

valve timing, electronic throttles,

oil-temperature sender, variable

tachometer warning segment, catalyst

protection & M Dynamic Driving Control

included in control strategy

Fuel requirement	Premium unleaded

Fuel capacity, U.S. gal.	14.5

Battery capacity, amp-hr.	70

Alternator output, amp./W	147/2058

## Drivetrain

Drive system	Front engine/rear drive

Manual transmission	ZF H, 6-speed

Ratios:	1st	4.35:1

2nd	2.50:1

3rd	1.66:1

4th	1.23:1

5th	1.00:1

6th	0.85:1

Reverse	3.93:1

Final drive ratio	3.62:1

## Chassis

Body/frame construction	Unitized steel structure with aluminum

hood

Front suspension	BMW M sport suspension; struts, arc-

shaped forged-aluminum lower arms,

coil springs, twin-tube gas-pressure

shock absorbers, anti-roll bar; alumi-

num thrust plate & strut-tower braces

Rear suspension	BMW M sport suspension; multi-link

system with Central Links, upper &

lower lateral links (upper link of cast

aluminum), coil  springs, twin-tube

gas-pressure shock absorbers, anti-roll

bar; steel thrust plate & V-brace

Steering type	Rack & pinion, engine-speed-sensitive

hydraulic power assist

Overall ratio	15.4:1

Turns, lock-to-lock	3.0

Turning circle, ft.	34.3

Compound, cross-ventilated

4-wheel disc brakes –

Diameter x thickness, mm/in.:

Front	345 x 28/13.7 x 1.10

Rear	328 x 20/12.9 x 0.79

Assist	Vacuum

Wheels	Cast alloy,

18 x 8.0 front/18 x 9.0 rear

Tires	Performance,

225/45ZR-18 front / 255/40ZR-18 rear

Stability-enhancement system	Dynamic Stability Control (DSC),

including all-speed traction control,

electronic brake proportioning,

antilock braking (ABS), cornering/

braking stability enhancement,

Dynamic Brake Control, Brake

Drying & Start-off Assistant;

plus M Variable Differential Lock

Performance data

Acceleration, 0-60 mph, sec. 	4.9

Top speed, mph 	155

Fuel economy, EPA est. MPG,

city/highway	16/24

#      #      #

# Footnotes

– Softtop lowered/raised; German DIN measurement.

– VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing.

– Due to low-profile tires, please note: Wheels, tires and suspension parts are more susceptible to road hazard and consequential damages. Z4 M models are not equipped with a spare tire and wheel. Performance tires are not recommended for driving in snow and ice conditions.

– BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.

– Electronically limited.

# Text boxes

Company

BMW of North America, LLC

BMW Group Company

Mailing address

PO Box 1227

Westwood, NJ

07675-1227

Office address

300 Chestnut Ridge Road

Woodcliff Lake, NJ

07677-7731

Telephone

(201)  307-3606

Fax

- 307-3607

Internet

bmwusa.com