| For Release: | May 22, 2006 |
| --- | --- |
| Contact: | David J. Buchko Product Communications Manager 201-307-3789 / dave.buchko@bmwna.com William Scully BMW Product Communications Specialist 201-307-3790 / william.scully@bmwna.com |

#### 2006 BMW Z4 COUPE 3.0si

## Technical Specifications

## General

Curb weight, lb.:

Manual transmission	3108

Automatic transmission	3156

Weight distribution, front/rear, %

Manual transmission	49.7/50.3

Automatic transmission	50.3/49.7

Wheelbase, in.	98.2

Track, front/rear, in.	58.0/60.0

Length, in.	161.1

Width, in.	70.1

Height, in. 	49.9

## Body

Type	2-seat Coupe

Aerodynamic drag coefficient	0.34

EPA size classification	2-Seater

## Accommodations

Seating capacity, persons	2

Shoulder room, in.	52.5

Head room, in.	37.3

Leg room, in.	42.0

EPA interior volume, cu ft.	47.6

Cargo volume, cu ft.	10.1/12.0

## Engine & electrical

Engine type	DOHC inline 24-valve 6-cylinder,

magnesium/aluminum composite

composite construction, Valvetronic

variable intake-valve lift & Double

VANOS  steplessly variable

intake- & exhaust-valve timing,

3-stage induction system

Bore x stroke, mm/in.	85.0 x 88.0/3.35 x 3.46

Displacement, cc/cu in.	2996/183

Compression ratio	10.7:1

Power @ rpm, hp	255 @ 6600

Torque @ rpm, lb-ft.	220 @ 2750

Engine-management system	MSV70 with knock control (2 sensors);

Valvetronic, variable valve timing,

electronic throttle system, engine

cooling & other functions included in

control strategy

Fuel requirement	Premium unleaded

Fuel capacity, U.S. gal.	14.5

Battery capacity, amp-hr.	55

Alternator output, amp./W	155/2170

## Drivetrain

Drive system	Front engine/rear drive

Manual transmission	Getrag H, 6-speed

Ratios:	1st	4.35:1

2nd	2.50:1

3rd	1.66:1

4th	1.23: 1

5th	1.00: 1

6th	0.85: 1

Reverse	3.93:1

Final drive ratio	3.46:1

## Drivetrain (cont.)

Automatic transmission	ZF 6 HP 19, 6-speed

Ratios:	1st	4.17:1

2nd	2.34:1

3rd	1.52:1

4th	1.14:1

5th	0.87:1

6th	0.69:1

Reverse	3.40:1

Final drive ratio	3.64:1

## Chassis

Body/frame construction	Unitized steel structure with aluminum

hood

Front suspension	Struts, arc-shaped forged-aluminum

lower arms with hydraulic cushions,

coil springs, twin-tube gas-pressure

shock absorbers, anti-roll bar;

aluminum thrust plate

Rear suspension	Multi-link system with Central Links,

upper & lower lateral links (upper link

of cast aluminum), coil  springs, twin-

tube gas-pressure shock absorbers,

anti-roll bar, steel thrust plate

& V-brace

Steering type	Rack & pinion, vehicle-speed-

sensitive electric power assist

Overall ratio	14.2:1

Turns, lock-to-lock	3.0

Turning circle, ft.	32.2

4-wheel ventilated disc brakes,

vacuum-assisted:

Diameter, front, mm/in.	325/12.8

Diameter, rear, mm/in.	294/11.6

Wheels (standard)	Cast alloy, 17 x 8.0

Wheels (optional)	Cast alloy, 18 x 8.0 front/18 x 8.5 rear

(ZSP)

ZSP – Sport Package

## Chassis (cont.)

Run-flat tires (standard)	225/45R-17 W-rated

Run-flat tires (optional)	225/40R-18 front / 255/35R-18 rear 3

W-rated (ZSP)

Stability-enhancement system	Dynamic Stability Control (DSC),

including all-speed traction control,

Dynamic Traction Control, electronic

brake proportioning, antilock braking

(ABS), cornering/braking stability

enhancement, Dynamic Brake

Control, Brake Fade Compensation,

Brake Standby, Brake Drying &

Start-off Assistant

## Performance data

Acceleration, 0-60 mph, sec. :

Manual transmission	5.6

Automatic transmission	5.7

Top speed, mph :

Manual transmission	155

Automatic transmission	155

Fuel economy, EPA est. MPG, city/highway:

Manual transmission	20/30

Automatic transmission	21/29

ZSP – Sport Package

# Footnotes

– Beneath cargo cover/cover retracted; German DIN measurement.

– VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing.

– Due to low-profile tires, please note: wheels, tires and suspension parts are more susceptible to road hazard and consequential damages. Z4 models are not equipped with a spare tire and wheel. Performance tires are not recommended for driving in snow and ice conditions.

– BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.

– Electronically limited.

# Text boxes

Company

BMW of North America, LLC

BMW Group Company

Mailing address

PO Box 1227

Westwood, NJ

07675-1227

Office address

300 Chestnut Ridge Road

Woodcliff Lake, NJ

07677-7731

Telephone

(201)  307-3606

Fax

- 307-3607

Internet

bmwusa.com