| For Release: | April 12, 2006 |
| --- | --- |
| Contact: | David J. Buchko Product Communications Manager 201-307-3789 / dave.buchko@bmwna.com William Scully BMW Product Communications Specialist 201-307-3790 / william.scully@bmwna.com |

### 2006 BMW Z4 M COUPE

# Standard & Optional Features

Performance & efficiency

3.2-liter DOHC 24-valve inline 6-cylinder engine:

High-pressure Double VANOS  steplessly variable intake- &

exhaust-valve timing	S

6 individual throttles, electronically controlled, with M Dynamic

Driving Control (Normal & Sport settings for throttles)	S

Machined intake ports & combustion chambers	S

Special BMW MS S70 electronic engine management system	S

Direct ignition system with pencil coils & knock control	S

Semi-dry-sump lubrication system	S

High-performance water pump with 3-dimensional vanes	S

BMW M low-back-pressure dual exhaust system	S

6-speed manual transmission with heavy-duty clutch	S

#### Handling, ride & braking

High-rigidity body/chassis unit with aluminum hood	S

BMW M strut-type front suspension with:

Unique forged lower arms	S

Front thrust plate, aluminum	S

Strut-tower braces	S

S – Standard

#### Handling, ride & braking (cont.)

BMW M Central Link rear suspension with:

Cast-aluminum upper transverse links	S

M3-type wheel bearings, Central Links, shock absorbers,

subframe mounting & other components	S

Rear thrust plate, steel	S

Subframe mounting braces	S

Front & rear anti-roll (stabilizer) bars	S

Twin-tube gas-pressure shock absorbers	S

Special BMW M suspension calibration (springs, shock

absorbers & anti-roll bars)	S

M Variable Differential Lock, cooled via NACA air intakes

in underbody	S

BMW M-calibrated Dynamic Stability Control (DSC), including

all-speed traction control, electronic brake proportioning,

antilock braking (ABS), cornering/braking stability enhancement,

Dynamic Brake Control, Brake Drying & Start-off Assistant	S

Engine-speed-sensitive variable-assist power steering	S

Compound, cross-ventilated 4-wheel disc brakes	S

M Double Spoke alloy wheels (design #224M ), 18 x 8.0 front/

18 x 9.0 rear; Extended Hump rims for retention of flat tire	S

225/45ZR-18 front / 255/40ZR-18 rear performance tires 	S

Flat Tire Monitor	S

#### Exterior design & function

Special BMW M front & rear body-color bumpers with

3 airscoops at front, diffusor at rear	S

Xenon headlights with auto-leveling & luminous rings	S

Automatic headlight control	S

Daytime Running Lamps	S

White turn-signal indicators 	S

S – Standard

#### Exterior design & function (cont.)

Rain-sensing windshield wipers	S

Heated windshield-washer jets	S

Heated outside mirrors	S

Side turn indicators behind BMW logos	S

BMW M logos on front fenders & trunklid	S

Adaptive Brake Lights	S

Exterior color selection including special M color, Imola Red	S

Metallic paint, including special M colors, Interlagos Blue

& Sepang Bronze	OPT

Chrome exhaust tips (4)	S

Ergonomics, luxury & convenience

Vehicle & Key Memory	S

Multi-function remote control incorporating selective

unlocking & remote trunk release	S

Special aluminum doorsill trims with M logo	S

Courtesy lights with fade-in/fade-out feature, actuation from

remote control & automatic switch-on when engine is turned off	S

Premium interior lighting 	ZPP

Cruise control	ZPP

Storage space in doors & behind seats , coinholder	S

Elastic nets on right side of center tunnel & on back of each seat	ZPP

Automatic-dimming interior & exterior mirrors	ZPP

Dual power/heated outside mirrors	S

Leather-wrapped tilt/telescopic M sport steering wheel with audio

controls, BMW M 3-spoke design with M color stitching	S

8-way M sport seats, including adjustable thigh support	S

8-way power M sport seats with driver’s-seat 	OPT/

memory (3 memory positions)	ZPP

Leather console kneepads & center armpad	S

3-stage, thermostatically controlled heated seats	OPT

S – Standard     OPT – Optional     ZPP – Premium Package

Ergonomics, luxury & convenience (cont.)

BMW M instrumentation with:

Red-on-gray pointers on analog dials	S

White illumination	S

Oil-temperature gauge	S

Variable warning segment on tachometer	S

LCD main & trip odometers	S

Service Interval indicator with miles-to-service readout	S

4-function On-board Computer, including

outside-temperature display	S

BMW On-board Navigation System	OPT

Nappa leather upholstery	S

M Extended Nappa leather upholstery, with additional leather

on doors, A-pillars, sun visors, center console

& center-rear storage compartment	OPT

Illuminated shift pattern on shift knob	S

Leather handbrake grip & shift knob	S

Brushed-aluminum interior trim	S

Carbon Leather interior trim	NC

Walnut Madeira wood interior trim	OPT

Velour floor mats	S

Power door windows with 1-touch open/close, anti-trapping

protection, push-to-lower/ pull-to-raise switches,

opening & closing from exterior door lock	S

Power side-window sealing system	S

Automatic climate control with activated-charcoal microfilter

ventilation & automatic recirculation control	S

Anti-theft AM/FM/CD/MP3 audio system with Radio Data System,

10 speakers including subwoofer	S

Premium, THX Certified audio system with upgraded audio power,

Carver technology, Digital Sound Processing,

10 audiophile-quality speakers incl. 2 subwoofers	ZPP

Pre-wiring for CD changer	S

6-disc CD changer	C

Sirius Satellite Radio	C

iPod adapter kit	C

S – Standard     OPT – Optional     NC – No extra cost     ZPP – Premium Package

C – BMW center-installed

Ergonomics, luxury & convenience (cont.)

Dual cupholders	S

## Illuminated glove compartment with silicon-damped hinges	S

Electric interior hatch release	S

Velour-lined cargo area	S

Retractable cargo cover	S

## Safety & security

Dual-airbag Supplementary Restraint

System with 2-stage Smart Airbags	S

Automatic safety-belt tensioners & force limiters	S

Active Knee Protection	S

OC3 seat-occupation detection on passenger’s seat	S

LATCH attachment for child-restraint safety seat, passenger’s seat	S

Disable switch for passenger’s-side airbag with indicator light	S

Side-impact airbags	S

Battery Safety Terminal	S

Automatic fuel-pump shutoff upon severe accident impact	S

Daytime Running Lamps	S 4

Advanced Crash Safety Management (ACSM)

for deployment of safety devices & systems	S

BMW Assist, including automatic collision notification, Assist

& SOS buttons, Bluetooth cellphone interface; enhanced	OPT/

Roadside Assistance & Customer Relations services	ZPP

Central locking system with double-lock anti-theft

feature, selective unlocking & interior locking

switch; also locks interior storage compartment	S

Coded Driveaway Protection	S

Pre-wiring for alarm system	S

Alarm system with operation from keyhead remote	C

S – Standard     OPT – Optional     C – BMW center-installed     ZPP – Premium Package

#      #      #

# Footnotes

– VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing.

– BMW produces and offers a large variety of wheels for its vehicles. Each has a Design Number.

– Due to low-profile tires, please note: Wheels, tires and suspension parts are more susceptible to road hazard and consequential damages. M models are not equipped with a spare tire and wheel. Performance tires are not recommended for driving in snow and ice conditions.

– Selectable via Vehicle Memory System (programming by BMW center).

– Includes footwells, separately switched left/right reading lights & storage compartments.

– Center compartment behind seats is included in central locking system.

# Text boxes

Company

BMW of North America, LLC

BMW Group Company

Mailing address

PO Box 1227

Westwood, NJ

07675-1227

Office address

300 Chestnut Ridge Road

Woodcliff Lake, NJ

07677-7731

Telephone

(201)  307-3606

Fax

- 307-3607

Internet

bmwusa.com