| For Release: | November 1, 2006 |
| --- | --- |
| Contact: | Thomas J. Plucinsky Product and Technology Communications Manager 201-307-3783 / thomas.plucinsky@bmwna.com William Scully BMW Product Communications Specialist 201-307-3790 / william.scully@bmwna.com |

2007 BMW M5

Product Highlights

General

•	Newest in a BMW M tradition that began in 1984 (US version introduced in 1988 model year); 4th-generation M5 (3rd generation was offered in U.S. in 2000-2003)

•	Sports car and luxury sedan in one exciting vehicle

•	Powered by a 5.0-liter, 500-hp V-10 engine via a 7-speed Sequential Manual Gearbox or 6-speed manual transmission

•	Produced in small numbers at BMW’s Dingolfing, Germany factory

•	Base price $83,195 including destination and handling charge

## Features that distinguish M5 from BMW 550i

Performance & efficiency

•	5.0-liter V-10 engine – 500 hp, 383 lb-ft. torque (previous M5: 4.9-liter V-8, 394 hp, 368 lb-ft.)

•	7-speed Sequential Manual Gearbox, first SMG designed “from scratch” as an SMG; incorporates DRIVELOGIC shift programming in evolved, refined form

- Optional (at no cost) 6-speed manual transmission

Handling, ride & braking

•	M Variable Differential Lock for enhanced traction and handling

•	Specially modified and calibrated front and rear suspension

•	Electronic Damping Control (EDC) – first appearance in a BMW M model; three modes (Comfort , Normal and Sport)

•	Special M5 steering system: “quicker” than 5 Series, two levels of Servotronic power assist tied to EDC modes

•	Compound, cross-ventilated disc brakes – BMW’s largest-dimensioned, most powerful brakes ever – with 2-piston front calipers

- 19 x 8.5 front/19 x 9.5 rear M Radial Spoke alloy wheels with 255/40ZR-19 front/ 285/35ZR-19 rear performance tires

•	BMW M-calibrated Dynamic Stability Control (DSC) with selectable M Dynamic Mode

•	MDrive (submenu in iDrive system): allows driver to combine personal preferences into a single setting, selectable via button on steering wheel –

•	Three levels of engine power and throttle response

•	SMG DRIVELOGIC shift-program settings

•	DSC modes and de-activation

•	EDC/steering settings

•	Settings of available Head-Up Display (standard or M)

•	Active Seat Backrest settings (three programs for optional M Multi-function 	Seats; see Options)

### Exterior design & function

•	Front bumper/spoiler/air-intake assembly

•	Traditional BMW M side “gills”

•	19-in. BMW M Double Spoke wheels

•	Unique rocker panels (side sills) with sharp accent line

•	Standard Satin Chrome Shadowline side-window trim

•	M exterior mirrors, shaped to enhance aerodynamics and reduce wind noise

•	Distinctively shaped lower section of trunklid

•	Rear bumper/spoiler/diffusor assembly

•	Four round stainless-steel exhaust outlets

•	Four unique BMW M colors

## Ergonomics, luxury & convenience

•	Doorsill trims with M5 logo

•	Unique speedometer and tachometer dials –

•	Red indicator needles

•	Specific scales (speedometer to 200 mph/300 km/h, tachometer to 9000 rpm)

•	M logo on tachometer face

•	Oil-temperature gauge in tachometer face

•	Power, DSC, EDC and SMG mode switches on center console

•	Short, illuminated SMG selector/shift lever or manual shift lever, depending on transmission

•	MDrive submenu in iDrive control system

- Real Time Traffic Information – 4-year subscription

•	Heated M sport front seats standard (16-way driver’s/14-way passenger’s power adjustment including 4-way lumbar)

•	Extended Leather upholstery with Merino leather, BMW’s finest grade –

•	Additional leather includes center section of instrument panel, center 	console/armrest, handbrake boot, upper door panels and door armrests

•	Full Leather and Perforated Full Leather optional

•	Unique BMW M color selection

•	Brushed Aluminum Shadow interior trim standard, choice of two optional woods

•	Anthracite-color headliner (with Perforated Leather or Full Leather interior, in Alcantara material)

Options

•	M Multi-function Comfort front seats with –

•	Active Backrests

•	Power shoulder support

•	Active head restraints

•	Active Seat Ventilation, including perforated leather upholstery (requires M Multi-function Comfort seats and Perforated Full Leather)

•	Comfort Access

•	Full Leather upholstery, with leather on expanded area of instrument panel; roof pillars and headliner in Alcantara material

•	Olive Ash Carrara wood interior trim (no extra cost)

•	Madeira Walnut red-brown wood interior trim (no extra cost)

•	M Head-up Display

•	Rear-spoiler delete

•	Power rear sunshade with manual rear side window sunshades

•	Split folding rear seats with ski bag

•	Heated rear seats

•	High Definition Radio

•	SIRIUS satellite radio

## BMW M powertrain details

•	500-hp V-10 engine delivers spectacular performance: 0-60 mph in 4.5 sec., top speed 155 mph (electronically limited):

•	Engine redline is 8250 rpm

•	10 individual, electronically controlled throttles

•	Ionic-current knock control

•	G-sensitive lubrication

•	Aluminum cylinder block and heads, ultra-rigid bedplate construction

•	7-speed Sequential Manual Gearbox with DRIVELOGIC offers driver 6 Sequential (manual) shift programs, 5 automated programs, and other functions for optimum performance and driving characteristics

•	Optional 6-speed manual transmission

## Safety & security

•	Dual front-impact 2-stage Smart Airbags with dual-threshold deployment

•	Interlocking door anchoring system for side impacts

•	Standard front-seat side-impact airbags

•	Optional rear-seat side-impact airbags and rear safety belts with automatic tensioners

•	Front and rear Head Protection System

•	Battery Safety Terminal – helps prevent possible short circuit after accident impact

- Tire Pressure Monitor

•	Coded Driveaway Protection for theft deterrence

•	Alarm system with interior motion detector

•	BMW Assist for 4 years – BMW’s comprehensive system of customer services and in-car telematics, standard

#      #      #

# Footnotes

– Due to low-profile tires, please note: Wheels, tires and suspension parts are more susceptible to road hazard and consequential damages. The M5 is not equipped with a spare tire and wheel. Performance tires are not recommended for driving in snow and ice conditions.