| For Release: | November 1, 2006 |
| --- | --- |
| Contact: | Thomas J. Plucinsky Product and Technology Communications Manager 201-307-3783 / thomas.plucinsky@bmwna.com William Scully BMW Product Communications Specialist 201-307-3790 / william.scully@bmwna.com |

2007 BMW M5

Technical Specifications

Bold within table indicates new specification for 2007

General

Curb weight, lb.	4012

Weight distribution, front/rear, %	52.2/47.8

Wheelbase, in.	113.7

Track, front/rear, in.	62.2/61.7

Length, in.	191.5

Width, in.	72.7

Height, in.	57.8

Body

Type	4-door sedan

Aerodynamic drag coefficient	0.31

EPA size classification	Midsize

Accommodations

Seating capacity, persons	5

Shoulder room, front/rear, in.	57.3/57.2

Head room, front/rear, in.	37.7/37.8

Leg room, front/rear, in.	41.5/36.0

EPA passenger-compartment volume, cu ft.	99.1

EPA cargo volume, cu ft.	14.0

Engine & electrical

Engine type	DOHC (4-cam) 40-valve V-10, high-

Pressure Double VANOS  steplessly

variable valve timing, 10 individual

electronically controlled throttles with

P400, P500 & P500 S settings

Bore x stroke, mm/in.	92.0 x 75.2/3.62 x 2.96

Displacement, cc/cu in.	4999/305

Compression ratio	12.0:1

Power @ rpm, hp	500 @ 7750

Torque @ rpm, lb-ft.	383 @ 6100

Engine-management system	MS S65 with ionic-current knock control,

variable valve timing, electronic throttles,

variable maximum power level, g-sensitive

lubrication system, oil-level/temperature

sender, variable tachometer warning 			segment, catalyst protection & other 			functions included in control strategy

Fuel requirement	Premium unleaded

Fuel capacity, U.S. gal.	18.5

Battery capacity, amp-hr.	90

Alternator output rating, amp./W	170/2380

Drivetrain

Drive system	Front engine/rear-wheel drive

Sequential Manual Gearbox  (SMG)	SMG III 247, electrohydraulically actuated,

electronically controlled 7-speed,

with 6 Sequential & 5 Automated shift

programs; twin-disc clutch

Ratios: 1st	3.99:1

2nd	2.65:1

3rd	1.81:1

4th	1.39:1

5th	1.16:1

6th	1.00:1

7th	0.83:1

Reverse	3.99:1

Drivetrain (cont.)

Manual transmission 	ZF Type G, 6-speed

Ratios: 1st	4.06:1

2nd	2.40:1

3rd	1.58:1

4th	1.19:1

5th	1.00:1

6th	0.87:1

Reverse	3.68:1

Final drive ratio	3.62:1

Chassis

Body/frame construction	Unitized; aluminum front end,

otherwise steel

Front suspension	BMW M sport suspension in

aluminum; struts, double-pivot lower

arms, coil springs, electronically

controlled twin-tube gas-pressure

shock absorbers with Normal,

Comfort & Sport modes, anti-roll

bar, subframe, thrust plate

Rear suspension	BMW M sport suspension in

aluminum; 4-link Integral system, coil

springs, electronically controlled twin-

tube gas-pressure shock absorbers

with Normal, Comfort & Sport modes,

anti-roll bar

Steering type	Rack &  pinion, Servotronic vehicle-

speed- sensitive power assist

with Comfort & Sport assist levels

Overall ratio	Variable; mean ratio is 12.4:1

Turning circle, ft.	40.7

4-wheel compound, ventilated &

cross-ventilated disc brakes:

Front, diameter x thickness, mm/in.	374 x 36/14.7 x 1.42

Front calipers	Aluminum

Rear, diameter x thickness, mm/in.	370 x 24/14.6 x 0.94

Rear calipers	Cast iron

Chassis (cont.)

Wheels	Light cast alloy, 19 x 8.5 front/19 x 9.5 rear

Tires	255/40ZR-19 front /

285/35ZR-19 rear

special performance

Stability-enhancement system	Dynamic Stability Control (DSC),

including all-speed traction control,

electronic brake proportioning,

antilock braking (ABS), cornering/

braking stability enhancement,

Dynamic Brake Control, Brake	 Standby,		Brake Drying, Start-off Assistant

& M Dynamic mode;

M Variable Differential Lock

# Performance data

Acceleration, 0-60 mph, sec. 	4.5

Top speed, mph	155

Fuel economy, EPA est. MPG, city/highway

7-speed SMG	12/18

6-speed manual transmission	12/18

#      #      #

# Footnotes

– Can be expanded via available folding rear seats.

– VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing.

– Available as a no-cost option

– Due to low-profile tires, please note: Wheels, tires and suspension parts are more susceptible to road hazard and consequential damages. The M5 is not equipped with a spare tire and wheel. Performance tires are not recommended for driving in snow and ice conditions.

– BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.

– Electronically limited.