2000 BMW 323Ci CONVERTIBLE & 323i SPORT WAGON

PRODUCT HIGHLIGHTS

General

·	Third step in the introduction of the all-new 3 Series.

·	Convertible and sport wagon join two sedan models and two coupe 	models.

·	Sedans – 323i and 328i (introduced in mid-1998 as 1999 models)

·	Coupes – 323Ci and 328Ci (introduced in 1999)

·	Dynamic Stability Control (DSC) standard on all models.

·	Extensive selection of stand-alone options and Packages, including 	Sport and Premium Packages and a Sport-Premium Package for 	323i 	sedan and sport wagon models.

The New 323Ci Convertible

·	Compared to predecessor model, all new.

·	Design based on 3 Series coupes.

·	Based on new E46 platform first introduced as 1999 323i and 328i sedans.

·	Priced significantly less than outgoing 323i convertible on a comparably 	equipped basis.

·	Cockpit is 10% roomier than predecessor.

·	Body structure is more rigid than predecessor, providing a more stable 	platform for improved handling and eliminating much of the “scuttle 	shake” normally associated with open-top cars.

·	New generation BMW Rollover Protection System incorporates pop-up 	rollbars in the rear, adjustable headrests.

·	Convertible top storage box can be folded when the top is up or off the car 	to increase trunk space.

·	Space saver spare tire is standard.

·	Seat-integrated safety belt system on front seats – introduced on 8 Series 	coupes

·	Extra controls at top of both front seat backs to facilitate access to rear 	seat.

·	Optional aluminum hardtop with front and rear individual reading lamps and 	electrically heated rear window.

·	Glass rear window on convertible soft-top.

·	Additional fore-and-aft power seat controls mounted on top of outside 	front seat backs to enhance access to rear seat.

The New 323i sport wagon

·	First time BMW has offered a 3 Series sport wagon in U.S. market.

·	Sport wagons are a growing part of the U.S. market as customers look for 	alternatives to SUVs.

·	Sport wagons offer active lifestyle drivers more versatile cargo space with 	the performance and handling of a sports sedan.

·	Roomier E46 3 Series sport wagon meets the special needs of this market 	better than its predecessors that were sold in other parts of the world.

·	Some view the sport wagon as the most handsome 3 Series, its extended 	roofline being the logical and more appealing shape for a four-door 	automobile.

·	Sport wagon is longer (+0.3 inches) and lower (-0.2 inches) than 323i 	sedan.

·	With rear split seats up, the sport wagon offers about 2.5 times more cargo 	space than the 323i sedan.

·	With rear seats folded flat – they fold absolutely flat – cargo space doubles 	to 48 cubic feet.

·	Standard space-saver spare tire provides room for convenient under-floor 	storage.

·	Full-size spare tire is optional; however, it reduces under-floor storage 	capacity.

·	12-volt power plug in cargo compartment.

·	Retractable cargo area cover and cargo/pet net.

·	Roof cargo rails are standard.

·	Tailgate and rear window open separately to provide low and wide access 	to cargo area.

·	Extended rear diffuser helps keep dirt from accumulating on rear window 	and tailgate handle.

Performance & Efficiency

·	2.5-liter, DOHC in-line six-cylinder engine.

·	Aluminum engine block with cast-iron cylinder liners.

·	Double VANOS11 VANOS = VAriable NOckenwellen Steuerung  = variable camshaft control, or variable valve timing. steplessly variable valve timing for intake and exhaust 	valves.

·	Dual resonance intake system with additional (third) turbulence intake 	passage.

·	Electronically controlled engine cooling.

·	Significantly enhanced torque in low- to mid-rpm range.

·	Smoother, quieter running, yet no loss of typical BMW sound.

·	Meets Low Emission Vehicle (LEV) standards.

·	Reduced maintenance requirements: approx. 15,000-mile interval22 BMW maintenance intervals are not fixed, but rather are determined by the Service Interval Indicator on the basis of how the vehicle is actually used and driven. for 	minor service, including oil and filter change; 100,000-mile spark plugs.

·	Both convertible and sport wagon available with five-speed manual or five-	speed automatic transmission.

·	Smooth-shifting manual transmission has self-adjusting clutch for longer 	clutch life, more consistent operation.

·	Automatic transmission with STEPTRONIC system; provides Sport mode 	and driver-selected up- and downshifts and Adaptive Transmission 	Control (ATC).

Handling, Ride & Braking

·	Ultra-rigid body structure for precise handling and outstanding ride 	comfort.

·	Strut-type front suspension with aluminum lower arms, optimized geometry 	and hydraulic cushions.

·	Multi-link rear suspension with aluminum transverse links.

·	Hydraulic mount for differential.

·	Rack-and-pinion steering with engine-speed sensitive power assist.

·	Four-wheel ventilated disc brakes with electronic front/rear proportioning, 	Anti-lock Braking System (ABS).

·	Dynamic Stability Control (DSC) for enhanced stability in severe cornering 	and accident-avoidance situations.

·	Optional sport suspension calibration on both models.

·	Standard 205/55R-16 91H all-season tires/16 x 7.0 cast alloy wheels.

·	Optional 225/45R-17 91W performance tires/17 x 8.0 cast alloy wheels.

Exterior & Aerodynamics

·	Masterful blend of traditional and new BMW design elements.

·	Traditional four headlights, with scallops and break-resistant covers.

·	Headlights approximately 30% more effective than before.

·	Xenon low-beam headlights optional on both convertible and sport wagon.

·	Foglights (standard on convertible, optional on sport wagon)

·	Windshield wipers shaped for effective operation, even at high speeds.

·	“Safety” outside door handle design: in body color and more easily pried 	open in a post-crash emergency.

·	Convertible has body-color side moldings.

Ergonomics, Luxury & Convenience

·	Standard multi-function remote-control security and central locking 	system, integrated into head of master key; includes two-step 	unlocking, remote trunk/tailgate release, opening of power windows 	and optional moonroof (on sport wagon), switch-on of interior lights, 	and arm/disarm optional alarm system.

·	Tilt/telescopic steering column.

·	Leather-wrapped steering wheel with fingertip multi-function controls 	(including standard cruise control, audio controls and optional 	accessory telephone) – four-spoke steering wheel standard on sport 	wagon, three-spoke sport steering wheel standard on convertible and 	optional on sport wagon.

·	Windshield wipers with adjustable and vehicle-speed sensitive wiping 	interval, single-wipe function.

·	BMW Ambiance Lighting: LED lights in roof bathe console area in soft 	orange light, helping occupants find controls at night.

·	Automatic climate control with microfilter ventilation, new automatic 	recirculation control.

·	Six-way manual front seats standard in sport wagon, six-way power front 	seats standard in convertible.

·	Eight-way power/two-way manual front sport seats with adjustable thigh 	support optional in convertible.

·	Ten-way power/two-way manual front sport seats with adjustable thigh 	support optional in sport wagon.

·	Interior trim in color high-gloss finish or Myrtle wood, according to optional 	packages.

·	Standard 10-speaker audio system; optional 10-speaker (sport wagon) or 	11-speaker (convertible) Harmon Kardon audio system including 	subwoofers.

·	Car and Key Memory allows drivers to personalize many electronic 	comfort, convenience and security features.

·	One-touch open/close operation of all windows – and optional moonroof 	on sport wagon – can also be opened or closed from the outside via 	the key in door lock; anti-trapping feature.

·	Sport wagon tailgate and rear window open separately, offering low and 	wide access to cargo area.

Safety & Security

·	Body structure engineered for excellent occupant protection in full and 	offset frontal impacts, side impacts and rear impacts.

·	Optimized steering column design for enhanced protection of driver in 	frontal impacts.

·	Dual-airbag front-impact Supplemental Restraint System (SRS) with two-	stage “smart” passenger-side airbag.

·	Front-seat side-impact airbags standard.

·	Front-seat Head Protection System (HPS) standard in sport wagon.

·	BMW Rollover Protection System (RPS) featuring pop-up rollbars 	integrated discreetly into the back of the rear headrests standard on 	convertible.

·	Battery safety terminal standard: after a severe impact, severs high-voltage 	connection between battery and starter cable to help prevent possible 	short circuit.

·	Differentiated airbag deployment system manages deployment of front-	impact airbags and front safety-belt tensioners in two thresholds of 	frontal impact severity.

·	The passenger-side airbag has two-stage “SMART” deployment depending

on the severity of the impact.

·	The system also automatically unlocks the doors and turns on the interior 	lights and the four-way hazard flashers after an accident impact.

Maintenance

·	Scheduled maintenance for three years/36,000 miles, whichever occurs 	first, included in base price.

·	Service Interval Indicator (SII), which computer-tracks actual vehicle use 	and custom-tailors maintenance recommendations accordingly, 	displays miles to next service.

·	Low-maintenance engine with hydraulic valve lifters, chain camshaft drive, 	long-life (100,000-mile) spark plugs.

·	Long-life engine air filter.

·	Extended engine-oil and filter change interval.

·	Stainless-steel exhaust system for corrosion resistance.

·	Self-adjusting clutch for longer clutch life (manual transmission).

·	True maintenance-free battery, engineered to need no topping-up during 	designed service life.

·	Brake pad condition easily inspected without removing wheels.

·	Easy replacement of ventilation filter.

·	No instrument cluster light bulbs, replaced by longer-lasting LEDs.