Contact:

David J. Buchko

BMW Product Communications Manager

201-307-3789 / dave.buchko@bmwna.com

Gordon B. Keil

BMW Product Communications Specialist

201-307-3790 / gordon.keil@bmwna.com

2003 BMW 3 Series 325i/xi Models

Standard & Optional Features

Bold within table indicates new feature for 2003.

Performance & efficiency	325i/xi	325i/xi

Sedan	Sport  Wagon

2.5-liter DOHC 24-valve inline 6-cylinder engine with –

Double VANOS – VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing. steplessly variable valve timing	S	S

Aluminum block & cylinder head	S	S

Dual resonance intake system	S	S

Electronic throttle system	S	S

Electronically controlled engine cooling	S	S

Direct ignition with knock control	S	S

5-speed manual transmission with direct 5th gear	S	S

5-speed STEPTRONIC  – BMW’s system of manual shift control for an automatic transmission. automatic transmission with

Adaptive Transmission Control & selectable Sport mode	OPT	OPT

Handling, ride & braking

Strut-type front suspension with forged-aluminum lower

arms, hydraulic cushions	S	S

S – Standard     OPT – Optional

Handling, ride & braking (Cont.)	325i/xi	325i/xi

Sedan	Sport Wagon

Rear subframe on 4 mounts, with acoustically decoupled

mounting of suspension system	S	S

Acoustically decoupled final drive with hydraulic rear mount	S	S

Front & rear anti-roll (stabilizer) bars	S	S

Twin-tube gas-pressure shock absorbers	S	S

Sport suspension calibration	ZSP/NA  – 325i/xi (where data for the two models differ).	ZSP/NA 3

Engine-speed-sensitive variable-assist power steering	S	S

4-wheel ventilated disc brakes	S	S

Dynamic Stability Control (DSC), including all-speed

traction control, Dynamic Traction Control (325i) or

Hill Descent Control (325xi), electronic brake propor-

tioning, antilock braking (ABS), Dynamic Brake Control

& cornering/avoidance stability enhancement	S	S

Fulltime all-wheel drive	NA/S	NA/S

16 x 7.0 alloy wheels, Star Spoke design #45  – BMW produces and offers a large number of wheel designs; each has a Design Number.	S	S

17 x 7.0 alloy wheels, Radial Spoke design #73	NA/ZSP	NA/ZSP

17 x 8.0 alloy wheels, Star Spoke design #96	ZSP/NA	ZSP/NA

205/55R-16 H-rated all-season tires	S	S

205/50R-17 V-rated all-season tires	NA/ZSP	NA/ZSP

225/45R-17 W-rated performance tires	ZSP/NA	ZSP/NA

Exterior & aerodynamics

Front & rear body-color bumpers	S	S

S – Standard     OPT – Optional     NA – Not available or not applicable

ZCW – Cold Weather Package     ZPP – Premium Package     ZSP – Sport Package

Exterior & aerodynamics (cont.)	325i/xi	325i/xi

Sedan	Sport Wagon

Halogen Free Form low-beam headlights	S	S

Bi-xenon headlights with auto-leveling	OPT	OPT

Automatic headlight control	ZPP	ZPP

Daytime running lamps	S  – Selectable via Vehicle Memory System (programming by BMW Center).	S 5

High-intensity headlight cleaning system	ZCW	ZCW

Halogen Free Form front foglights	S	S

2-speed + intermittent windshield wipers, adjustable &

car-speed-sensitive interval, single-wipe operation	S	S

Rain-sensing windshield wipers	ZPP	ZPP

Heated windshield-washer jets	S	S

Park Distance Control	NA	OPT

Metallic paint	OPT	OPT

Chrome grille slats	NA	S

Ergonomics, luxury & convenience

Vehicle & Key Memory	S	S

Keyless entry with multi-function remote control	S	S

Selective unlocking	S 5	S 5

Remote trunk/tailgate release	S	S

Opening of windows & moonroof	S	S

Dual power/heated outside mirrors	S	S

Automatic-dimming inside rearview mirror	ZPP	ZPP

BMW Universal Transceiver (garage-door opener)	C	C

S – Standard     OPT – Optional     C – BMW Center-installed

NA – Not available or not applicable     ZPP – Premium Package     ZSP – Sport Package

Ergonomics, luxury & convenience (cont.)	325i/xi	325i/xi

Sedan	Sport Wagon

Courtesy lights with fade-in/fade-out feature, actuation

from remote control, automatic switch-on when engine

is turned off, separately controlled left/right front & rear

reading lights, front footwell lighting & illuminated visor

vanity mirrors	S	S

BMW Ambiance Lighting	S	S

Locking glove compartment with take-out flashlight	S	S

Leather-covered tilt/telescopic steering wheel with

fingertip cruise, audio & phone controls:

385 mm/4 spokes	S	S

375 mm/3 spokes	ZSP	ZSP

6-way adjustable front seats	S	S

8-way power front seats with 3-position driver’s-seat

& outside-mirror memory  – Also includes automatic tilt-down of right outside mirror for backing up.	OPT/ZPP	OPT/ZPP

10-way front sport seats	ZSP	ZSP

8-way power + 2-way manual front sport seats	OPT	OPT

with 3-position driver’s-seat & outside-mirror memory 6	ZPP+ZSP  – When Premium & Sport Packages are combined, or when stand-alone power-seats option & Sport Package are combined.	ZPP+ZSP 7

Fold-up front center armrest with storage compartment	S	S

3-stage, thermostatically controlled heated front seats	OPT/ZCW	OPT/ZCW

Electronic analog instrumentation

with servo-motor operation	S	S

LCD main & trip odometers	S	S

Service Interval Indicator with miles-to-service readout	S	S

Check Control monitor system (pictogram display)	S	S

4-function Onboard Computer	OPT/ZPP	OPT/ZPP

S – Standard     OPT – Optional

ZCW – Cold Weather Package     ZPP – Premium Package     ZSP – Sport Package

Ergonomics, luxury & convenience (cont.)	325i/xi	325i/xi

Sedan	Sport Wagon

BMW Onboard Navigation System with DVD database	OPT  – Requires Premium Package or Onboard Computer.	OPT 8

Montana leather upholstery (seating surfaces, door trim,

handbrake grip & boot, manual shift-lever boot)	OPT	OPT

Leather shift knob	S	S

Titanium-finish interior trim	S	S

Myrtle wood interior trim	OPT/ZPP	OPT/ZPP

Power windows with 1-touch open/close, anti-trapping

feature, opening from remote, opening & closing

from exterior lock	S	S

Automatic climate control with microfilter ventilation

& automatic recirculation control	S	S

2-way power moonroof with sliding interior shade, wind

deflector, 1-touch open/close, opening from remote,

opening & closing from exterior lock	OPT/ZPP	S

Anti-theft AM/FM/CD audio system with Radio Data

System, diversity antenna system & pre-wiring for

auxiliary audio input	S	S

Harman Kardon audio system with upgraded speakers

including subwooofers, vehicle-speed-sensitive

equalization & Spatial Enhancement  – Includes all features of standard system; subwoofers in Sedan only.	OPT	OPT

Cassette player instead of in-dash CD player	NC	NC

Pre-wiring for CD changer	S	S

6-disc CD changer	C	C

Pre-wiring for BMW Cellular Phone System	S	S

BMW Cellular Phone System	C	C

Dual front cupholders	S	S

S – Standard     OPT – Optional     NC – No-cost option     C – BMW Center-installed

NA – Not available or not applicable     ZCW – Cold Weather Package

Ergonomics, luxury & convenience (cont.)	325i/xi	325i/xi

Sedan	Sport Wagon

Console storage compartment	S	S

Seatback storage nets	S	S

Fold-up center rear armrest	OPT  – Included with leather upholstery and/or folding rear seats.	S  – Includes storage compartment, dual cupholders & center head restraint.

Split folding rear seats	OPT	S

Ski bag	OPT  – Included with folding rear seats.  /ZCW ZCW

Safety & security

Fully finished trunk with reversible floor mat to keep smaller

cargo from sliding, drop-down toolkit	S	S

accessory electrical outlet	NA	S

Fully finished, carpeted variable cargo compartment with

floor straps, retractable cover, cargo net &

Interior trunk or tailgate release	S	S

Full-use spare wheel & tire (alloy wheel)	S	OPT

Dual-airbag Supplementary Restraint System

with 2-stage Smart Airbags	S	S

Height-adjustable front safety belts with automatic

tensioners & force limiters	S	S

Head restraints at all seating positions	S	S

Automatic-locking retractors (ALR) on all passenger

safety belts (for installation of child restraint seats)	S	S

Interlocking door anchoring system for side impacts	S	S

Front-seat Head Protection System (HPS)	S	S

Front-seat side-impact airbags	S	S

Rear-seat side-impact airbags	OPT	OPT

Integrated deployment logic for safety-belt tensioners,

airbags & post-impact safety measures	S	S

S – Standard     OPT – Optional     C – BMW Center-installed

Safety & security (cont.)	325i/xi	325i/xi

Sedan	Sport Wagon

Battery Safety Terminal	S	S

Central locking system with double-lock anti-theft

feature, selective unlocking	S	S

Coded Driveaway Protection	S	S

Pathway Lighting	S 5	S 5

Pre-wiring for alarm system	S	S

Alarm system with operation from keyhead remote,

motion detector	C	C

S – Standard     OPT – Optional     C – BMW Center-installed