Contact:

David J. Buchko

BMW Product Communications Manager

201-307-3789 / dave.buchko@bmwna.com

Gordon B. Keil

BMW Product Communications Specialist

201-307-3790 / gordon.keil@bmwna.com

2003 BMW 325 Sedan and Sport Wagon
 Specifications

Bold within table indicates new specification relative to corresponding 2002 model.

General	325i	325xi	325i	325xi

Sedan	Sedan	Sport Wagon	Sport Wagon

Curb weight, lb.:

Manual transmission	3219	3461	3362	3594

Automatic transmission	3307	3527	3450	3627

Weight distribution, front/rear, %:

Manual transmission	50.3/49.7	52.6/47.4	47.7/52.3	50.1/49.9

Automatic transmission	50.9/49.1	53.0/47.0	48.4/51.6	50.0/50.0

Wheelbase, in.	107.3  – Specification applies to all models.

Track, front/rear, in.	57.9/58.4	57.9/58.3	57.9/58.4	57.9/58.3

Length, in.	176.0	176.0	176.3	176.3

Width, in.	68.5	68.5	68.5	68.5

Height, in.	55.7	56.5	55.5	56.3

Body

Type	Unitized all-steel structure 1

Aerodynamic drag coefficient	0.31	0.31	0.32	0.32

EPA size classification	Compact	Compact	Small station	Small station

wagon	wagon

Accommodations	325i	325xi	325i	325xi

Sedan	Sedan	Sport Wagon	Sport Wagon

Seating capacity, persons	5	5	5	5

Shoulder room, front/rear, in.	54.4/54.2	54.4/54.2	54.4/54.2	54.4/54.2

Head room, front/rear, in.:

without moonroof	38.4/37.5	38.4/37.5	NA	NA

with moonroof	37.0/37.4	37.0/37.4	37.0/37.6	37.0/37.6

Leg room, front/rear, in.	41.4/34.6	41.4/34.6	41.4/34.4	41.4/34.4

EPA interior volume, cu ft.	90.8	90.8	90.7	90.7

EPA cargo volume, cu ft. 	10.7  – Can be expanded via folding rear seats (optional Sedans, standard Sport Wagons & Coupe, NA Convertible).	10.7 3	25.7  – Rear seats upright, cargo loaded to ceiling. With standard space-saver spare, an additional volume of 2 cu ft. is available under the cargo floor. More volume available with rear seats folded.	27.3 4

Engine & electrical

Engine type	DOHC inline 24-valve 6-cylinder, Double VANOS steplessly variable valve timing 1

Bore x stroke, mm/in.	84.0 x 75.0 / 3.31 x 2.95 1

Displacement, cc/cu in.	152/2494 1

Compression ratio	10.5.1 1

Power @ rpm, hp	184 @ 6000 1

Torque @ rpm, lb-ft.	175 @ 3500 1

Engine-management system	Siemens MS 43 with knock control (2 sensors); variable valve timing, electronic throttle system, dual resonance intake system, engine cooling & other functions included in control strategy 1

Fuel requirement	Premium unleaded 1

Fuel capacity, U.S. gal.	16.6 1

Battery capacity, amp-hr.	80 1

Alternator output rating, amp./W	120/1680 1

NA – Not available or not applicable.

Drivetrain	325i	325xi	325i	325xi

Sedan	Sedan	Sport Wagon	Sport Wagon

Drive system	Front engine/	Front engine/	Front engine/	Front engine/

rear-wheel	all-wheel	rear-wheel	all-wheel

drive	drive	drive	drive

Manual transmission	5-speed 1
		Getrag B	ZF C	Getrag B	ZF C

Ratios:

1st	4.23:1	4.21:1	4.23:1	4.21:1

2nd	2.52:1	2.49:1	2.52:1	2.49:1

3rd	1.66:1	1.66:1	1.66:1	1.66:1

4th	1.22:1	1.24:1	1.22:1	1.24:1

5th	1.00:1	1.00:1	1.00:1	1.00:1

Reverse	4.04:1	3.85:1	4.04:1	3.85:1

Final drive ratio	3.15:1	3.23:1	3.46:1	3.23:1

Automatic transmission	5-speed STEPTRONIC with Adaptive Transmission Control & selectable Sport mode 1:

ZF 5 HP 19	GM 5	ZF 5 HP 19	GM 5

Ratios:

1st	3.67:1	3.45:1	3.67:1	3.45:1

2nd	2.00:1	2.21:1	2.00:1	2.21:1

3rd	1.41:1	1.59:1	1.41:1	1.59:1

4th	1.00:1	1.00:1	1.00:1	1.00:1

5th	0.74:1	0.76:1	0.74:1	0.76:1

Reverse	4.10:1	3.17:1	4.10:1	3.17:1

Final drive ratio	3.46:1 1

Chassis	325i	325xi	325i	325xi

Sedan	Sedan	Sport Wagon	Sport Wagon

Body/frame construction	Unitized steel 1

Front suspension	Struts, arc-shaped forged-aluminum lower arms with hydraulic cushion, coil springs, twin-tube gas-pressure shock absorbers, anti-roll bar 1

Sport Packages, 325Ci Coupe std., Sport Package except 325xi models:	sport suspension calibration

Rear suspension	Multi-link system with Central Links, upper & lower lateral links (upper link of cast aluminum), coil springs, twin-tube gas-pressure shock absorbers, anti-roll bar 1

Sport Packages, 325Ci Coupe std., Sport Package except 325xi models:	sport suspension calibration

Steering type	Rack & pinion, engine-speed-sensitive power assist 1

Overall ratio	13.7:1 1

Turns lock-to-lock	3.0 1

Turning circle, ft.	34.4	35.8	34.4	35.8

4-wheel ventilated disc brakes:

Diameter, front, mm/in.	300/11.8	300/11.8	300/11.8	300/11.8

Diameter, rear, mm/in.	294/11.6	294/11.6	294/11.6	294/11.6

Wheels (standard)	Cast alloy, 16 x 7.0 1:

Wheels (optional)	Cast alloy 1:

17 x 8.0	17 x 7.0	17 x 8.0	17 x 7.0

(Sport Pkg.)	(Sport Pkg.)	(Sport Pkg.)	(Sport Pkg.)

Tires (standard)	All-season, 205/55R-16 H-rated 1

Tires (optional) 	All-season, 205/50R-17 V-rated (Sport Package, xi models) Performance, 225/45R-17 W-rated (Sport Package, all other models)

Chassis (Cont.)	325i	325xi	325i	325xi

Sedan	Sedan	Sport Wagon	Sport Wagon

Stability-enhancement system	Dynamic Stability Control (DSC), including all-season traction control, Dynamic Traction Control (325i/Ci models) or Hill Descent Control (325xi models), electronic brake proportioning, antilock braking (ABS) & Cornering/avoidance-stability enhancement 1

Performance data

Acceleration, 0-60 mph  – BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times., sec.,

manual transmission	7.1	7.6	7.4	7.8

automatic transmission	8.1	8.8	8.5	9.0

Top speed, mph  – Electronically limited.	128 1

Fuel economy, EPA est. MPG,

city/highway:

manual transmission	20/29	19/27	20/29	19/26

automatic transmission	20/28	19/26	20/28	19/26