Contact:

David J. Buchko

BMW Product Communications Manager

201-307-3789 / dave.buchko@bmwna.com

Gordon B. Keil

BMW Product Communications Specialist

201-307-3790 / gordon.keil@bmwna.com

2003 BMW 330 coupe and convertible

Specifications

Bold within table indicates new specification relative to corresponding 2002 model.

General	330Ci	330Ci

coupe	convertible

Curb weight, lb.:

Manual transmission	3285	3616

Automatic transmission	3362	3704

Weight distribution, front/rear, %:

Manual transmission	50.1/49.9	48.7/51.3

Automatic transmission	50.6/49.4	49.4/50.6

Wheelbase, in.	107.3  – Specification applies to all models.

Track, front/rear, in.	57.9/58.4	57.9/58.4

Length, in.	176.7	176.7

Width, in.	69.2	69.2

Height, in.	54.0	54.0  – With softtop raised.

Body

Type	Unitized all-steel structure 1

Aerodynamic drag coefficient	0.32	0.35

EPA size classification	Sub-compact	Mini-compact

Accommodations	330Ci	330Ci

coupe	convertible

Seating capacity, persons	5	4

Shoulder room,

front/rear, in.	54.5/52.7	54.5/45.9

Head room, front/rear, in.:

without moonroof	37.5/36.5	38.0/36.4 2

with moonroof	36.3/36.2	NA

Leg room, front/rear, in.	41.7/33.2	41.7/32.0

EPA interior volume, cu ft.	84.4	80.0 2

EPA cargo volume, cu ft.	9.5 3	7.7  – With softtop lowered. Volume with softtop raised & variable softtop compartment adjusted is approximately 15% greater.

Engine & Electrical	330Ci	330Ci
		coupe	conv.

Engine type	DOHC inline 24-valve 6-cylinder, Double VANOS steplessly variable valve timing 1

Bore x stroke, mm/in.	84.0 x 89.6 / 3.31 x 3.53 1

Displacement, cc/cu in.	2979/182 1

Compression ratio	10.2.1 1

Power @ rpm, hp	225 @ 5900 1

Torque @ rpm, lb-ft.	214 @ 3500 1

Engine-management system	Siemens MS 43 with knock control (2 sensors); variable valve timing, electronic throttle system, dual resonance intake system, engine cooling & other functions included in control strategy 1

Fuel requirement	Premium unleaded 1

Fuel capacity, U.S. gal.	16.6 1

Battery capacity, amp-hr.	80 1

Alternator output rating, amp./W	120/1680 1

Drivetrain	330Ci	330Ci
		coupe	convertible

Drive system	Front engine/	Front engine/

rear-wheel drive	rear-wheel drive

Manual transmission	ZF Type C, 5-speed 1

Ratios:	1st	4.21:11

2nd	2.49:11

3rd	1.66:11

4th	1.24:11

5th	1.00:11

Reverse	3.85:11

Final drive ratio	2.93:1	3.07:1

Automatic transmission	5-speed STEPTRONIC with Adaptive Transmission Control & selectable Sport mode 1:

ZF 5 HP 19	ZF 5 HP 19

Final drive ratio	2.93:1 1

Ratios:	1st	3.67:1	3.67:1

2nd	2.00:1	2.00:1

3rd	1.41:1	1.41:1

4th	1.00:1	1.00:1

5th	0.74:1	0.74:1

Reverse	4.10:1	4.10:1

Final drive ratio	3.38:1	3.38:1

Chassis	330Ci	330Ci
		coupe	convertible

Body/frame construction	Unitized steel 1

Front suspension	Struts, arc-shaped forged-aluminum lower arms with hydraulic cushion, coil springs, twin-tube gas-pressure shock absorbers, anti-roll bar 1

330Ci coupe std., 330Ci convertible Sport Package: sport suspension calibration

Rear suspension	Multi-link system with Central Links, upper & lower lateral links (upper link of cast (aluminum), coil springs, twin-tube gas-pressure shock absorbers, anti-roll bar 1 330Ci coupe std., 330Ci convertible Sport Package: sport suspension calibration

Steering type	Rack & pinion, engine-speed-sensitive power assist 1

Overall ratio	13.7:1 1

Turns lock-to-lock	3.0 1

Turning circle, ft.	34.4	34.4

4-wheel ventilated disc brakes:

Diameter, front, mm/in.	325/12.8 1

Diameter, rear, mm/in.	320/12.6 1

Wheels (standard)	Cast alloy, 17 x 7.0 1

Wheels (optional)	Cast alloy, 17 x 7.5 front / 17 x 8.5 rear (330i/Ci Sport Package). Cast alloy, 17 x 7.0 (330xi Sport Pkg., run-flat tire option all models). Cast alloy, 18 x 8.0 front / 18 x 8.5 rear (option requiring Sport Pkg., 330i/Ci models)

Chassis (cont.)	330Ci	330Ci
		coupe	convertible

Tires (standard)	All-season, 205/50R-17 H-rated 1

Tires (optional)	Performance, 225/45R-17 front / 245/40R-17 rear Z-rated (330i/Ci Sport Package) Run-flat option all models, run-flat 205/50R-17 V-rated Performance, 225/40R-18 front / 255/35R-18 rear Z-rated (option requiring Sport Package, 330Ci models)

Stability-enhancement system	Dynamic Stability Control (DSC), including all-speed traction control, Dynamic Traction Control (330Ci models), electronic brake proportioning, antilock braking (ABS) & cornering/avoidance-stability enhancement

Performance data

Acceleration, 0-60 mph  – BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.,

manual transmission	6.4	6.9

automatic transmission	7.0	7.5

Top speed, mph  – Electronically limited.	128 1

Fuel economy, EPA est. MPG,

city/highway:

manual transmission	21/30	20/28

automatic transmission	20/28	19/27