IMMEDIATE

David J. Buchko

BMW Product Communications Manager

201-307-3789 / dave.buchko@bmwna.com

Gordon B. Keil

BMW Product Communications Specialist

201-307-3790 / gordon.keil@bmwna.com

2004 BMW 5 Series

Technical Specifications

General	525i	530i	545i

Curb weight, lb.:

Manual transmission	3428	3472	3803

Sequential Manual Gearbox

(SMG) 1	3450	3494	3814

Automatic transmission	3450	3494	3814

Weight distribution, front/rear, %:

Manual transmission	49.8/50.2	50.8/49.2	50.3/49.7

Sequential Manual Gearbox

(SMG) 1	50.2/49.8	51.1/48.9	51.4/48.6

Automatic transmission	50.2/49.8	51.1/48.9	51.4/48.6

GVWR, lb.:

Manual transmission	4530	4575	4905

Sequential Manual Gearbox

(SMG) 1	4552	4597	4916

Automatic transmission	4552	4597	4916

Wheelbase, in.	113.7 2

Track, front/rear, in.	61.3/62.3 2,3

Length, in.	190.6 2

Width, in.	72.7 2

Height, in.	58.0 2

Ground Clearance, in.	4.5 (3.9 in. with Sport Package) 2

1 – Delayed availability.

2 – Specification applies to all models.

3 – With standard wheels.

Body	525i	530i	545i

Type	4-door sedan 2

Aerodynamic drag coefficient	0.29 2

EPA size classification	Compact 2

Accommodations

Seating capacity, persons	5 2

Shoulder room, front/rear, in.	57.3/57.2 2

Head room, front/rear, in.	37.7/37.9 2

Leg room, front/rear, in.	41.5/36.0 2

EPA interior volume, cu ft.	99.1 2

EPA cargo volume, cu ft.	14.0 2

Engine & electrical

Engine type	DOHC inline 24-valve	DOHC 32-valve

6-cylinder, Double VANOS 4	(4-cam) V-8,

steplessly variable intake- &	Valvetronic variable

exhaust-valve timing 5	valve lift & Double

VANOS 4 steplessly

variable intake- &

exhaust-valve timing

Bore x stroke, mm/in.	84.0 x 75.0/	84.0 x 89.6/	92.0 x 82.7/

3.31 x 2.95	3.31 x 3.53	3.62 x 3.26

Displacement, cc/cu in.	2494/152	2979/182	4398/268

Compression ratio	10.5:1	10.2:1	10.5:1

Power @ rpm, hp	184 @ 6000	225 @ 5900	325 @ 6100

Torque @ rpm, lb-ft.	175 @ 3500	214 @ 3500	330 @ 3600

Engine-management system	Siemens MS 43 5		Motronic ME9

Fuel requirement	Premium unleaded 2

Fuel capacity, U.S. gal.	18.5 2

Battery capacity, amp-hr.	80 5		90

Alternator output, amp./W	120/1680 5		170/2380

2 – Specification applies to all models.

4 – VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing.

5 – Specification applies to 525i & 530i.

Drivetrain	525i	530i	545i

Drive system	Front engine/rear drive 2

Manual transmission	ZF Type H,		ZF Type G,

6-speed 5		6-speed

Ratios: 	1st	4.35:1 5		4.06:1

2nd	2.50:1 5		2.40:1

3rd	1.66:1 5		1.58:1

4th	1.23:1 5		1.19:1

5th	1.00:1 5		1.00:1

6th	0.85:1 5		0.87:1

Reverse	3.93:1 5		3.77:1

Final drive ratio	3.15:1	2.93:1	2.93:1

Sequential Manual Gearbox 1	Electrohydraulic/electronic controls applied to 6-

speed manual transmission, ratios as for Type H

or Type G as appropriate to model; includes Dynamic

Driving Control (Sport button) affecting shift

characteristics & engine response to accelerator pedal

Automatic transmission	ZF 6 HP 19 5		ZF 6 HP 26

6-speed STEPTRONIC with Adaptive Transmission

Control, selectable Manual & Sport modes 2

Ratios:	1st	4.17:1 2

2nd	2.34:1 2

3rd	1.52:1 2

4th	1.14:1 2

5th	0.87:1 2

6th	0.69:1 2

Final drive ratio	3.73:1	3.46:1	3.38:1

1 – Delayed availability.

2 – Specification applies to all models.

5 – Specification applies to 525i & 530i.

Chassis	525i	530i	545i

Body/frame construction	Unitized; aluminum front end, otherwise steel

Front suspension	Struts, double-pivot lower arms, coil springs, twin-

tube gas-pressure shock absorbers, anti-roll bar;

aluminum suspension system & subframe (OZSP: sport

suspension calibration, Active Roll Stabilization) 2

Rear suspension	4-link Integral suspension, coil springs, twin-tube gas-

pressure shock absorbers, anti-roll bar; aluminum

suspension system & subframe (OZSP: sport

suspension calibration, Active Roll Stabilization) 2

Steering type	Rack & pinion, engine-speed-sensitive power assist 2

(OZSP: Active Steering with Servotronic vehicle-

speed-sensitive power assist)

Overall ratio, standard steering	Mechanically variable; mean ratio is 14.1:1 2

Overall ratio, Active Steering	Electrically/electronically  variable over wide range of

10:1 – 18:1 2

Turning circle, ft.	37.5 2

4-wheel ventilated disc brakes

with aluminum calipers:

Front, diameter x thickness,	310 x 24/	324 x 30/	348 x 30/

mm	12.2 x 0.94	12.8 x 1.18	13.7 x 1.18 6

Rear, diameter x thickness,	320 x 20/	320 x 20/	345 x 24/

mm	12.6 x 0.79	12.6 x 0.79	13.6 x 0.94 6

Assist	Vacuum 2

Wheels: 	standard	Lightweight	Cast alloy,	Cast alloy,

forged alloy,	17 x 7.5	17 x 7.5

16 x 7.0

optional (OZSP)	Cast alloy,	Cast alloy,	Cast alloy,

17 x 8.0	18 x 8.0	18 x 8.0 front/

18 x 9.0 rear

2 – Specification applies to all models.

6 – Compound rotors, aluminum/cast-iron construction.

OZSP – Sport Package

Chassis (cont.)	525i	530i	545i

Tires:	standard	225/55R-16	225/50R-17	225/50R-17

V-rated	V-rated	V-rated

all-season	all-season	all-season

optional (OZSP)	245/45R-17	245/40R-18	245/40R-18 F/

W-rated run-flat	W-rated run-flat	275/35R-18 R

performance	performance	W-rated run-flat

performance

Stability-enhancement system	Dynamic Stability Control (DSC), including Dynamic

Traction Control, electronic brake proportioning,

antilock braking (ABS), Dynamic Brake Control &

cornering/braking stability enhancement 2

Performance data	525i	530i	545i

Acceleration, 0-60 mph, sec.: 7

manual transmission or SMG 1	7.8	6.6	5.7

automatic transmission	8.2	6.9	5.8

Top speed, mph:

manual transmission or SMG	146	150 8	150 8

automatic transmission	144	150 8	150 8

Fuel economy, EPA est. MPG, city/highway:

manual transmission	19/28	20/30	17/25

SMG		21/30	20/29	16/24

automatic transmission	19/28	19/29	18/26

1 – Delayed availability.

2 – Specification applies to all models.

7 – BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.

8 – Electronically limited.

OZSP – Sport Package   F – Front   R – Rear    TBD – To be determined.