IMMEDIATE

David J. Buchko

BMW Product Communications Manager

201-307-3789 / dave.buchko@bmwna.com

Gordon B. Keil

BMW Product Communications Specialist

201-307-3790 / gordon.keil@bmwna.com

2004 BMW 6 Series

Specifications

General	645Ci	645Ci
		Coupe	Convertible

Curb weight, lb.:

Manual transmission	3781	4178

Sequential Manual Gearbox

(SMG)	3792	4189

Automatic transmission	3792	4189

Weight distribution, front/rear, %:

Manual transmission	51.6/48.4	48.3/51.7

Sequential Manual Gearbox

(SMG)	51.7/48.3	48.4/51.6

Automatic transmission	51.7/48.3	48.4/51.6

GVWR, lbs	4619

Wheelbase, in.	109.4

Track, front/rear, in.	61.3/62.7 1

Length, in.	190.2 1

Width, in.	73.0 1

Height, in.	54.1 1

Body	645Ci	645Ci
		Coupe	Convertible

Type	2-door coupe	2-door convertible

Aerodynamic drag coefficient	0.30	0.32

EPA size classification	Subcompact	Subcompact

Accommodations

Seating capacity, persons	4	4

Shoulder room, front/rear, in.	56.4/49.4 1

Head room, front/rear, in.	37.3/35.5	37.8/36.7

Leg room, front/rear, in.	42.0/28.8 1

EPA interior volume, cu ft.	81.0	82.0

EPA cargo volume, cu ft.	13.0	12.4/10.6

Engine & electrical

Engine type	DOHC 32-valve (4-cam) V-8, Valvetronic

variable valve lift & Double VANOS  steplessly

variable intake- & exhaust-valve timing 1

Bore x stroke, mm/in.	92.0 x 82.7/3.62 x 3.26 1

Displacement, cc/cu in.	4398/268 1

Compression ratio	10.5:1 1

Power @ rpm, hp	325 @ 6100 1

Torque @ rpm, lb-ft.	330 @ 3600 1

Engine-management system	Motronic ME9 with knock control; variable

valve lift & timing, electronic throttle system,

steplessly variable intake system, engine cooling

& other functions included in control strategy 1

Fuel requirement	Premium unleaded 1

Fuel capacity, U.S. gal.	18.5 1

Battery capacity, amp-hr.	110 1

Alternator output rating, amp./W	170/2380 1

Drivetrain	645Ci	645Ci
		Coupe	Convertible

Drive system	Front engine/rear-wheel drive 1

Manual transmission	ZF Type G, 6-speed 1

Ratios:	1st	4.05:1 1

2nd	2.40:1 1

3rd	1.58:1 1

4th	1.19:1 1

5th	1.00:1 1

6th	0.87:1 1

Reverse	3.68:1 1

Final drive ratio	3.23:1	3.46:1

Sequential Manual Gearbox 	Electrohydraulic/electronic controls applied to

6-speed manual transmission (above);

transmission & final drive ratios same as for

manual transmission 1

Automatic transmission	ZF 6 HP 26, 6-speed STEPTRONIC with Adaptive

Transmission Control, selectable Sport & Manual

modes 1

Ratios:	1st	4.17:1 1

2nd	2.34:1 1

3rd	1.52:1 1

4th	1.14:1 1

5th	0.87:1 1

6th	0.69:1 1

Reverse	3.40:1 1

Final drive ratio	3.46:1 1

Chassis	645Ci	645Ci
		Coupe	Convertible

Body/frame construction	Unitized; aluminum front-end structure, aluminum

hood & doors, thermoplastic front fenders,

Sheet Molding Compound (SMC) trunklid 1

Front suspension	Struts, double-pivot lower arms, coil springs,

twin-tube gas-pressure shock absorbers, Active

Roll Stabilization; aluminum suspension system,

thrust plate & subframe 1 (Convertible: additional

diagonal braces)

Rear suspension	4-link Integral suspension, coil springs, twin-tube

gas-pressure shock absorbers, Active Roll Stabili-

zation; aluminum suspension system & subframe 1

(Convertible: additional diagonal braces)

Steering type	Rack & pinion, Servotronic vehicle-speed-sensitive

variable power assist 1

Overall ratio	Mechanically variable; mean ratio is 14.4:1 1

Overall ratio, Active Steering	Electrically/electronically variable over wide range

(Sport Package)	of 10:1 – 18:1 1

Turning circle, ft.	37.4 1

Brakes	4-wheel ventilated discs with lightweight aluminum/

cast-iron rotors, aluminum front/ cast-iron rear

calipers 1

Diameter, front, mm/in.	348/13.7 1

Diameter, rear, mm/in.	345/13.6 1

Wheels (standard)	Cast alloy, 18 x 8.0 1

Wheels (optional)	Cast alloy, 19 x 8.5 front/19 x 9.0 rear

(Sport Package) 1

Tires (standard)	245/45R-18 V-rated run-flat all-season 1

Tires (optional)	245/40R-19 front / 275/35R-19 rear

W-rated run-flat performance (Sport Package) 1

Stability-enhancement system	Dynamic Stability Control (DSC); includes Dynamic

Traction Control, electronic brake proportioning,

antilock braking (ABS), Dynamic Brake Control

& cornering/braking stability enhancement 1

Performance data	645Ci	645Ci
		Coupe	Convertible

Acceleration, 0-60 mph, sec. :

Manual transmission	5.5	6.0

Sequential Manual Gearbox

(SMG)	5.5	6.0

Automatic transmission	5.7	6.1

EPA estimated MPG, city/highway:

Manual transmission	17/25	15/23

Sequential Manual Gearbox

(SMG)	16/24	15/22

Automatic transmission	18/26	18/26

# Footnotes

– Specification applies to both models.

– With standard wheels.

– With softtop raised.

– Softtop raised/lowered, variable softtop storage compartment adjusted accordingly.

– VANOS = VAriable NOckenwellen Steuerung = variable camshaft control, or variable valve timing.

– Delayed availability.

– 1 – BMW AG test results. Actual acceleration results may vary depending on specification of vehicle; road and environmental conditions; testing procedures and driving style. These results should be used for comparison only, and verification should not be attempted on public roads. BMW urges you to obey all posted speed limits and to please wear your safety belt at all times.